## Slide 1: Ethical Hacking – Lecture 3
John Black Fall 2020

## Slide 2: Get Kali
Get the latest Kali
  2020.3 is current
  Ch 7 of our book is helpful; so is google
    90% of 2nd ed of the book is on google books
    Please don’t pirate it
Install as an iso
3 GB Download
  Direct or Torrent
  offensive-security has VMWare/Vbox images
    3.5-3.7 GB
    These are much preferred since they have guest addons

## Slide 3: Basics:
  At install-time there is only the root acct, passwd toor
  $ ifup eth0 to bring up networking
    Must be root
    This is usually on by default now
    For VMware player, set to NAT which provides DHCP
    Don’t recommend using a public-facing IP unless you really know what you’re doing
    There is a wiki on the kali site

## Slide 4: Get Kali (cont)
Change root passwd
Create a user
  Risky to always be root, though I sometimes will do this
  Put this user in admin or sudo
update-alternatives --config editor
  $ echo “set sw=4 ic nows ai” > ~/.exrc
  Etc etc etc
sudo apt-get update
sudo apt-get upgrade
  sudo apt-get dist-upgrade

## Slide 5: Next Up: Networking Review
We’ll quickly review networking basics now
Relevant tools: host, lsof, netstat, ifconfig, tcpdump, nc, nmap
Some resources on our web page if you’re rusty
  Basic network programming in python
  The book has some stuff

## Slide 6: Two main transport protocols
UDP
  Just IP with ports
  Best effort
    DHCP, DNS, FTP, NFS
TCP
  World-famous three-way handshake
  Guaranteed delivery
  Guaranteed in-order (sliding windows)
    ssh, http

## Slide 7: Pack it Up!
Message
UDP Header
Src IP, Dest IP, Len, Chksm, TTL
Src Port, Dest Port, Len, Chksm
Eth Header
IP Header
Src addr, Dest addr, Chksm
Ethernet addresses are called “MAC addresses”
Ethernet checksum is actually appended to end of packet

## Slide 8: Steps Involved in Sending That Packet
DNS, ARP, 802.3, IP forwarding, NAT, BGP
  Yell out what these do

## Slide 9: Local Routing Table
Our local routing table (on host of user1) is not going to have a route to IP of user2
  Routing table will therefore send our packet to the gateway
  Gateway is the machine/router on the “edge” of the network responsible for processing all incoming/outgoing traffic from/to the LAN
    NAT boxing, firewalling, and other stuff is usually done here as well

## Slide 10: Getting to the Gateway
How to we route to the IP address of the gateway on our local Ethernet?
  ARP (Address Resolution Protocol)
    Translates IP addresses into MAC addresses
    Caches old lookups, so we probably already have the MAC address of the gateway
    If not, we send an ARP Request to the LAN, including the IP address whose MAC we seek
    Owner (ie, the gateway) sends ARP Reply with his MAC address and we cache it
      Usually, all other machines who hear the ARP Reply cache it as well
      Leads to attacks…

## Slide 11: Sending to the Gateway
Now we have the MAC address of the gateway
  Send our packet to the gateway via the Ethernet protocol
  This is usually done with a hardware device (network card) which often puts the Eth header on your packet for you, computes checksums, etc.
    Broadcasts packet, detects collisions
    Exponential backoff
    Promiscuous mode – Sniffers use this
      Works through hubs, but doesn’t work through switches on a switched Ethernet
      You can often fool switches (see: Ettercap)

## Slide 12: tcpdump and wireshark
Promiscuous mode
  Libpcap
NIDS use libpcap, IPS use iptables/netfilter

## Slide 13: Gateway Receives Eth Packet
Strips Eth header and again tries to route the resulting IP packet
  Looks in routing table, sends to ISP
  ISP probably routes using BGP
  Reaches other ISP
    Note that we’re using other Ethernets and similar layer-2 protocols for each hop!
  Other ISP routes to other LAN’s gateway
    Gateway sees IP is in its range and does ARP to route to user2

## Slide 14: User2 Receives Packet
User2 receives the IP packet
  Removes IP header
    No one else (is supposed to) look inside packet until user2 receives it
    NAT boxes break this rule
    Firewalls break this rule
  Sees it’s a UDP packet and “sends” to proper port
  Ports are mapped to applications via listento() in C
    Application receives message and processes it

## Slide 15: Other Protocols
We didn’t even talk about SLIP or PPP
ATM, FDDI, Wireless
What about DHCP?
  Dynamic IP addresses
There is also ICMP
  Internet Control Message Protocol
  Echo (ping), traceroute
Application Layer Protocols
  SNMP – Network Management
  SMTP – Sendmail
  POP/IMAP – Mail protocols

## Slide 16: IP – Best Effort Datagrams
IP is “best effort”
  There is no tracking of packets
  If something is dropped… oh well
  If one fragment is dropped, many transport layer protocols (like TCP) will consider the whole thing lost and not ACK
  This seems bad, but it’s one of the biggest successes of IP
  UDP is IP with ports, so it too is “best effort”

## Slide 17: TCP – Transmission Control Protocol
Stateful connections
  Runs over IP just like UDP, but adds more than just ports
  Establish a connection with accept() and connect() in C
    Uses famous “three-way handshake”
  Reliable delivery
    Unlike best-effort, this protocol guarantees delivery of packets, in proper order
    Uses sequence numbers, sliding windows, ACKs every transmission

## Slide 18: Programming TCP
Server side goes first
  Create STREAM socket
  Bind to address/port
  Listen
  Accept connections
    A connection gives you another socket that you communicate on
Client (much simpler)
  Create a STREAM socket
  Connect to address/port
I’m expecting you’ve written such programs before

## Slide 19: Netcat aka nc
Self-described “swiss-army knife” of networking
  Usually voted in top 5 of “top security tools” at http://sectools.org/
In the old days we used telnet
  nc is far more powerful and flexible
  Let’s go play…