## Slide 1: Ethical Hacking – Lecture 5
John Black Fall 2020

## Slide 2: Why Port Scan?
Depending on context of your pen testing
  “Host Discovery”
If you have a single host, or a specified list of hosts
  You can forgo this part
Note: sysadmins often scan their own networks
  Find out which hosts are up
  What ports are open
  Are firewalls working properly
  Etc…

## Slide 3: Legality, Sensitivity
Port scanning is legal in the U.S.
  Court ruling from 2000
Is often considered pre-cursor to break-ins however
People have gone to jail
Some ISPs forbid it
  Mine does
Some Universities forbid it
  Yours does
Our machines are scanned all the time
  Millions of script kiddies

## Slide 4: The nmap Utility
nc can port scan
  -z flag
nmap is a much more powerful tool however
Included on kali of course
  Scan from dial-up or wireless hotspot
    Better yet, get permission first
  Don’t scan from your ISP or CU
nmap is complex, but the basics aren’t bad…

## Slide 5: nmap -sL (simply List)
nmap -n -sL 192.168.10.0/30
Omitting -n means we’ll do Reverse DNS lookups
  Handy because names can have meanings (fw-cu)
  Unlikely these scans would be noticed
$ nmap -sL research/26
Host fs-net.cs.colorado.edu (128.138.242.192) not scanned
Host cs-gw3-fs.cs.colorado.edu (128.138.242.193) not scanned
Host 128.138.242.194 not scanned
Host locust.cs.colorado.edu (128.138.242.195) not scanned
Host alumni.cs.colorado.edu (128.138.242.196) not scanned
Host mroe-fs.cs.colorado.edu (128.138.242.197) not scanned
….

## Slide 6: Scanning Technology
Old school: just ping
  ICMP echo: they HAVE to respond… it’s in the RFC!
  Lots of hosts won’t respond
  Hitting lots of hosts on a network might trip alarms
    There are ways to hide this with proxies and non-aggressive timing
nmap -sP (simply Ping)
  -PE means use ICMP echo (code 7)

## Slide 7: Traditional Ping of Various Hosts
$ sudo nmap -sP -PE -R -v yahoo.com google.com citibank.com target.com facebook.com amazon.com
Starting Nmap 5.00 ( http://nmap.org ) at 2010-12-04 23:43 MST
Host ir1.fp.vip.ac4.yahoo.com (67.195.160.76) is up (0.049s latency).
Host 74.125.227.20 is up (0.019s latency).
Host citibank.com (192.193.103.222) is down.
Host wap.target.com (161.225.130.163) is down.
Host www-11-01-ash2.facebook.com (69.63.189.16) is up (0.045s latency).
Host 210-250.amazon.com (72.21.210.250) is down.
Nmap done: 6 IP addresses (3 hosts up) scanned in 0.66 seconds
Raw packets sent: 9 (252B) | Rcvd: 3 (84B)

## Slide 8: Need a New Approach
Send a TCP SYN?
  To what port? 80?
  Send raw SYN?
    Need root (Unix) or WinPCap (Windows XP and after)
    Send SYN, if SYN/ACK, port is open; if RST it’s closed
      nmap only cares (for now) that the machine is alive
    Known as “half-open scanning”
    Use nmap -PS<port list> // 80 is default
  sudo nmap -sP -PS80 -R -v yahoo.com google.com citibank.com target.com facebook.com amazon.com
  Host ir1.fp.vip.sk1.yahoo.com (72.30.2.43) is up (0.029s latency).
  Host 74.125.227.18 is up (0.019s latency).
  Host citibank.com (192.193.219.58) is up (0.021s latency).
  Host m.target.com (161.225.130.163) is up (0.046s latency).
  Host www-10-01-ash2.facebook.com (69.63.189.11) is up (0.046s latency).
  Host 166-252.amazon.com (207.171.166.252) is up (0.045s latency).
  If no privs, you have to use connect()
    Full handshake—takes longer, less control
    Less likely to crash various TCP stacks, however

## Slide 9: ACK Ping Instead?
Send ACK (ie, ACK flag set in TCP Header)
  If you get RST, the machine is alive…. gg!
  Many firewalls will drop incoming SYNs to closed ports, so SYN/connect scans will fail
  Many firewalls will allow ANY source port to make outbound connections so will not filter incoming ACKs
    The --syn option on iptables
  Unf many firewalls these days are stateful (--state on iptables)
    A firewall knows if there is a connection on a given port and drops ACKs if the connection is closed
    $ sudo nmap -sP -PA www.microsoft.com
    Note: Host seems down. If it is really up, but blocking our ping probes, try -PN
    $ sudo nmap -sP -PA www.colorado.edu
    Host www.colorado.edu (128.138.129.98) is up (0.00091s latency).

## Slide 10: UDP Pings?
nmap –PU<port list> // default 31338
  Why is default port so weird?
  nmap sends an empty packet
  If we see ICMP Port Unreachable, host is up
  Other errors (host unreachable, TTL exceeded) or silence is interpreted as host unreachable/down
    UDP is sometimes firewalled more heavily, sometimes less
    If you know an application is running on a UDP port, you can leverage this
      Eg, DNS uses UDP on port 53

## Slide 11: Wait, just ARP scan!
Isn’t using ARPRequests faster than using TCP?
  To scan IPs, you have to get their MAC addr, right?
  Usually faster, but the problem is…?
nmap uses ARP by default if you’re on the LAN and have privs
  Use --send-ip if you don’t want this
  Use -PR to force it (requires ethernet)

## Slide 12: nmap -sP
-sP means “simply Ping”
By default, nmap will send an ICMP echo and an ACK to port 80 (or connect(), which means SYN, if you don’t have privs)
research 66% nmap -sP research/26
Starting Nmap 4.11 ( http://www.insecure.org/nmap/ ) at 2010-12-04 23:17 MST
Host cs-gw3-fs.cs.colorado.edu (128.138.242.193) appears to be up.
Host summit200-ot1.cs.colorado.edu (128.138.242.200) appears to be up.
Host summit200-ot2.cs.colorado.edu (128.138.242.201) appears to be up.
Host summit200-cs1.cs.colorado.edu (128.138.242.202) appears to be up.
Host summit200-st1.cs.colorado.edu (128.138.242.203) appears to be up.
Host dell-cr1b15b.cs.colorado.edu (128.138.242.204) appears to be up.
Host watchman.cs.colorado.edu (128.138.242.210) appears to be up.
Host research-rac.cs.colorado.edu (128.138.242.224) appears to be up.
Host research.cs.colorado.edu (128.138.242.225) appears to be up.
Host www-apps.cs.colorado.edu (128.138.242.232) appears to be up.
Host fip.cs.colorado.edu (128.138.242.235) appears to be up.
Host supervillain.cs.colorado.edu (128.138.242.249) appears to be up.
Nmap finished: 64 IP addresses (12 hosts up) scanned in 0.701 seconds
research 67%

## Slide 13: Ports often open
80 – http
25 – smtp
22 – ssh
443 – https
21 – ftp
113 – auth
23 – telnet
53 – DNS
554 – rtsp
3389 – ms-term-server
1723 – pptp (ms vpn)
389 – ldap
636 – ldapssh
256 – FW1-securemote (checkpoint firewall-1 admin port)

## Slide 14: Decent Host Disc Strategy
-PE -PP
-PS21,22,23,25,80,113,31339
-PA80,113,443,10042
Should catch the vast majority of hosts
  -PE is ICMP echo; -PP is ICMP timestamp
Might be worthwhile to add --source-port 53
  DNS replies come from port 53
  Often 88 works too (Kerberos) or 67 (DHCP)

## Slide 15: Forego Host Discovery?
nmap -PN <ip list>
  -PN means “don’t ping”
  If you already know list of hosts
  If you’re worried about alarms from ping sweep
Takes forever
  nmap has to wait for responses from 65536 ports with no RTT estimate from the ping phase
  Each non-response has to be resent in case something was dropped

## Slide 16: Port Scanning
Once you have nailed down which hosts to scan
  -sS is most effective (default SYN scan)
    Requires privs again
    Called a “stealth scan”
    Send SYN, get SYN/ACK (if port is open for TCP), send RST
      If we send ACK instead, then we have to send FIN, etc…
      If we do nothing, target will resend SYN/ACKs (bad)
    Send SYN, get RST, port is closed
    Send SYN, get nothing, resend, still nothing, port is filtered
  -p<port_list> says which ports to scan
    Default is 1000 most popular ports from nmap’s list

## Slide 17: Stuff we don’t have time for
nmap can do a ton of other kinds of scans
  Including UDP, Maimon, Xmas, Idle etc
    Idle scans are ultra clever and quite stealthy
    You find an idle 3rd party machine called the “zombie”
    Get the zombie’s IP ID (fragment number)
    SYN to target with source IP set to zombie
    Get the zombie’s IP ID and see if it incremented

## Slide 18: Idle Scan (port open)

## Slide 19: Version Detection
nmap can do OS versioning as well
  # nmap -O
    Uses peculiarities in how various OSes implement TCP/IP stack
    Seems to think Ubuntu 10.04 server is OS X??
nmap can do service versioning as well
  # nmap -A
    Complex mix of response types, banners, etc.
    If an SSL port, nmap will handshake and try to find the service behind it

## Slide 20: Version Detection
root@kali:~# nmap -T4 -A -p80,443 www.amazon.com
PORT STATE SERVICE VERSION
80/tcp open http?
| robots.txt: has 48 disallowed entries (15 shown)
----------
443/tcp open ssl/https?
|_http-methods: No Allow or Public header in OPTIONS response (status code 301)
| robots.txt: has 48 disallowed entries (15 shown)
----------
Warning: OSScan results may be unreliable because we could not find at least 1 open and 1 closed port
Device type: general purpose|storage-misc|webcam
Running (JUST GUESSING) : Apple Mac OS X 10.5.X (97%), BlueArc embedded (93%), DVTel embedded (88%)
Aggressive OS guesses: Apple Mac OS X 10.5.5 (Leopard) (97%), BlueArc Titan 2100 NAS device (93%), DVTel DVT-9540DW network camera (88%)
No exact OS matches for host (test conditions non-ideal).
Network Distance: 2 hops
TRACEROUTE (using port 80/tcp)
HOP RTT ADDRESS
1 0.12 ms 192.168.189.2
2 0.06 ms 72.21.211.176